## Slide 1
CMSC 591
Robotic Vision
Notes: 1

## Slide 2: Graph SLAM Introduction
He (David) Zhang
Notes: Today I will give a lecture about graph slam,

## Slide 3: What is Graph?
Definition: Graph is an abstract data structure that consists of a finite set of nodes (or vertices) and set of edges which connect a pair of nodes.
How graph is defined in the case of robot navigation, SLAM ?
Notes: What is Graph, the definition. The graph structure is very useful. Based on the meaning/model of the nodes and the edges, the graph structure is used in various applications. A common example is to find out the shortest path from one place to another, where each node represents a location while an edge contains the distance between two locations. Another application is infectious prevention, where each node represents a person while an edge contains some value indicating how close these two persons are, e.g. family members, or colleagues. If one person caught the virous, by running a clustering algorithm on this graph structure, we can instantly find out who are the potential infected person that need to be tested.
Now, the question is, how the graph is represented in the case of robot navigation, more specifically, slam. To answer this question, we need to recap a bit about SLAM.

## Slide 4: SLAM – Simultaneous Localization and Mapping
Given a Robot with multiple sensors, at the same time:
  Build a Map (model) of the environment
  Estimate the Location of the robot in the Map
Notes: It’s essentially a chicken-and-egg problem, we need the map to localize the robot and we need the location of the robot to integrate the sensor’s measurement to construct the map.
So, generally, SLAM is not a one time deal, it’s an incremental process where we assume the first location is known and we repeatedly build the map and estimate the robot’s pose in the map as the robot travels around the environment.

## Slide 5: SLAM – Simultaneous Localization and Mapping
LiDAR (2D/3D)
Camera (Monocular/Stereo), RGB-D camera
Wheel odometry
IMU (gyroscope, accelerometer)
GPS
Notes: To achieve this, sensors are installed on a robot to capture the information of the map. There are many different types of the sensors, including . No sensor is perfect, and their measurements contain noise. So, in practice, not one but several sensors will be used to solve the SLAM problem, it is also known as a sensor fusion problem.

## Slide 6: Measurement constraint
10 meters
20 meters
Graph SLAM is a framework that integrates the measurement constraints to infer the robot’s pose and the map (landmarks) of the environment.
Notes: Each measurement gives us some information about the robot’s location. There is a term called measurement constraint, that means this measurement will constrain the estimation of the robot pose in a certain space . For example, if a robot receives a wifi signal sent by a router, from the signal strength, we can infer that the robot must be somewhere whose distance to the router is around certain meters. Meanwhile, it detects a wall whose distance is 20 meters away, from which we know the robot stay somewhere within the red rectangle. By combining these two, we know the robot is most likely in one of these two yellow areas. If there is another measurement, like GPS, showing the robot is in somewhere within the blue circle, then we can confidently say that the robot is most likely at this smaller purple area. So, each measurement will constrain the robot’s pose estimation to a smaller space. More measurements provide more information that can be used to infer the robot’s pose more accurately.
Graph SLAM is a framework that integrate the sensors’ measurements to infer the robot’s pose and the map of the environment.
The question is how to fuse the sensors’ measurements to compute the map and the robots’ pose?
One way to solve this problem is graph SLAM approach.

## Slide 7: Graph SLAM
Landmark measurement
  Node: robot pose (Localization) or landmark position (Map)
  Edge: measurement constraint
Notes: In Graph SLAM, each node represents a robot pose or a landmark position. The landmark is an abstract term and it can be a visual feature, an object, a 3D point, depending your sensors and the methods you use.
The edge contains the measurement information that constrain the estimation of the robot pose and landmark positions.
For example, a robot observes a landmark. The simple graph mode has two nodes, xt and lk, and an edge connecting them.

## Slide 8: Graph SLAM
Odometry measurement
  Node: robot pose (Localization) and landmark position (Map)
  Edge: measurement constraint
Notes: Here, at the timestamp t, the robot moves. In the graph, there are two nodes xt and xt+1 and one edge containing an odometry measurement ut,t+1

## Slide 9: SLAM Problem
Landmark measurement
Odometry measurement
Localization
Mapping
…
…
Notes: Let’s put these two together.
The robot take a measurement from the environment, it is a landmark measurement that it observes a door. More specific, it could include many visual features like corner points or SIFT points. Here we just use this object for demonstration. As it moves to next position, it sees previous landmark and a new landmark plant. Then it moves again, and observes a plant.
And the odometry measurement and the landmark measurement are not perfect and they have noise.
As the robot moves along its trajectory, its pose estimation error accumulates. When it sees a previous landmark, this error can be reduced.
一般SLAM 的问题

## Slide 10: Graph SLAM
How to compute the values of given
…
…

## Slide 11: Graph Optimization
Nodes (𝜇)
Edges
Multiplication of the probability density functions defined on the Edges
Odometry Constraint
Landmark Constraint
Prior Constraint
Notes: This figure shows a simple example, which gives us a glimpse of the graph structure. The nodes in the graph stand for robot poses and landmark positions. And the edges connecting the nodes are the constraints, either odometry constraint or landmark constraint.
in reality, the process will involve hundreds and thousands of robot poses and landmarks, and also it includes many loops
The structure of the graph will be very complex, then how to solve this problem?

## Slide 12
Conditional joint probability
P(AB|C) P(A|BC)P(B|C)
Bayes Rule: P(A|B) P(B|A)P(A)
Conditional Bayes Rule: P(A|BC) P(B|AC)P(A|C)
=
=
=

## Slide 13: Graph SLAM Solution
,
…
For one-dimension case and assume Gaussian distribution model
…
Directly Solution for linear system
Notes: What is a graph model? Let’s reuse previous example. Assume a robot moves from x0 to x2, and perceives two landmarks. Its graph structure is shown here. The red nodes stand for robot poses and the green for landmarks. The lines between them represent constraints: odometry constraints and landmark constraints. Each constraint represent a probability model. For example, assuming gaussian noise, p(u01) , now we want to estimate the value for variables x0 x1 x2 l0 and l1 that maximize the likelihood of the joint probability of this graph structure. By using log operation and remove the constant items, this maximize likelihood problem is converted into a nonlinear least square problem. The vector e incorporates residual error of each constraint, where sigma contains the corresponding measurement variance. Then it can be solved using an iterative nonlinear optimization method like gauss newton, gradient descendent or Levenberg–Marquardt algorithm. The linearized version can be represented by a matrix A and a vector b. A is called measurement jacobian and b include entries of the residual for each constraint. Later we will explain how they are constructed.

## Slide 14: A Concrete Example for graph construction
GPS
Notes: Sensor fusion

## Slide 15: Example: A linear case
Initial Constraint
Odometry Constraint
Landmark Constraint
Q: how many constraints in this graph?
6
= 8
Notes: Graph SLAM will collect all these constraints, and use them to find out the most likelihood estimations for the robot poses and landmark positions that fulfill these constraints. Just imagine the constraint as a rubber band, the optimization process is to stretch or shrink these rubber bands, to find the best solution.

## Slide 16: Linear Case
Matrix A
Vector b
1
-1
1
-1
-10
10
When we add measurement, make sure the coefficient of the row variable is positive
=8
Notes: To solve this problem, what we do here is to build a matrix and a vector that come from these constraints. We build a quadratic matrix, the row and column stand for the poses and landmarks. And every time we make an observation, say a odometry u01, this will affect locally four elements in the matrix. Here the robot moves from x0 to x1, given u01,
Means x1 = x0 + 10, it has two ways to the matrix. First, x0 – x1 = -10, second, we let x1 be positive, in the second row, we have –x0 + x1 equal to 10. One rule here is that keep the diagonal entries positive and another is that the constraints are locally addictive to the corresponding entries. OK, based on these two rules, if the robot moves from x1 to x2 given u12, may I ask you what are the values in the matrix will be like? Let me give you a hint, the constraint u12 only affects the entries in these red boxes.

## Slide 17: Example
 |  | -1 | 1 | 
 |  | -1 | 1 | 
-3
Matrix A
Vector b
1
-1
2
-1
-10
13
-1
=8
When we add measurement, make sure the coefficient of the row variable is positive
Notes: The second row will become, -x0 + 2 x1 – x2 = 13, where does it come from? It is derived by summing u01 and u12 together with x1 is positive. Exactly like this equation, x1 – x2 + x1 – x0 = 3 + 10 = 13
The third row will become –x1 + x2 = -3 which is exact the same with u12.
Then what will happen by adding landmark constraint m00? The affected entries are contained in the green boxes?

## Slide 18: Example
 |  |  |  | -1
 |  | -1 | 1 | 
 | -1 |  |  | 1
 |  |  |  | -1
 |  | -1 | 1 | 
 | -1 |  |  | 1
-3
15
Matrix A
Vector b
2
-1
2
-1
-25
13
-1
=8
When we add measurement, make sure the coefficient of the row variable is positive
Notes: The first row will become 2x0 – x1 – l0 = -25, the fourth row will become –x0 + l0 = 15, pretty easy, right?

## Slide 19: Example
 | 2 | -1 | 0 | -1
 | -1 | 3 | -1 | -1
 | 0 | -1 | 2 | -1
 | -1 | -1 | -1 | 3
 | 2 | -1 | 0 | -1
 | -1 | 3 | -1 | -1
 | 0 | -1 | 2 | -1
 | -1 | -1 | -1 | 3
-25
8
-11
28
Matrix A
Vector b
Did we miss something?
=8
Notes: Similarly, when we add all these constraints, the matrix A and vector b. Remember matrix A corresponds to measurement jacobian and b include residuals for each constraint. Then the magic part for graph slam is that the direct solution is inverse A times vector b, mu contains the robot poses x and landmark positions.
Therefore the major step for graph slam is that you keep adding the constraints into the jacobian matrix and the residual vector. When you done with that, you just need a very simple operation, then outcomes the best estimation for the robot poses and landmark positions.

## Slide 20: Example
 | 3 | -1 | 0 | -1
 | -1 | 3 | -1 | -1
 | 0 | -1 | 2 | -1
 | -1 | -1 | -1 | 3
 | 3 | -1 | 0 | -1
 | -1 | 3 | -1 | -1
 | 0 | -1 | 2 | -1
 | -1 | -1 | -1 | 3
-27
8
-11
28
Matrix A
Vector b
= 8
Notes: Similarly, when we add all these constraints, the matrix A and vector b. Remember matrix A corresponds to measurement jacobian and b include residuals for each constraint. Then the magic part for graph slam is that the direct solution is inverse A times vector b, mu contains the robot poses x and landmark positions.
Therefore the major step for graph slam is that you keep adding the constraints into the jacobian matrix and the residual vector. When you done with that, you just need a very simple operation, then outcomes the best estimation for the robot poses and landmark positions.

## Slide 21: Example
8
3
15
5
2
Notes: Now, constraints in the graph are valued as shown in the right, from which we can easily calculate the values of the poses and landmark positions. With x0 equal to 2, x1 8, x2 5, what is the value of l0. Now let’s verify whether the matrix solution can output the these values.

## Slide 22: Example
8
7
A: x2 > 5
B: x2 = 5
C: x2 < 5
A: l0 > 13
B: l0 = 13
C: l0 < 13
A: x1 > 8
B: x1 = 8
C: x1 < 8
A: x0 > -2
B: x0 = -2
C: x0 < -2
3
15
5
2
3
15
5
2
B A A C
Notes: Now let’s modify this graph a little bit, here the observation between x2 and l0 is not 8 but 7, then what’s the output of x2 and l0? I give you three options. X2 is larger than 5, while l0 is less than 13
Why ? Let’s recall the idea of rubber band. The rubber band between x2 and l0 is become shorter, which needs to pull these two nodes together so, the x2 is pulled towards right while l0 to the left. This picture does not explain it well since it is 2D picture, but in 1D it is exact what’s happening.
X0 is the only absolute constraint, all the other are relative constraints, no matter what these relative constraints change, they put no influence to the value of the x0. It is always -2.
X2 and l0 are pulled closer, while the rubber band between x0 and x1, x1 and x2 are stretch out.
How does this happen? This is where the magic of graph slam plays. There are loops in the graph structure which might not added up. Because of motion noise and measurement noise. What graph slam does, by computing A inverse times b, we find the best solution to the relaxation of those rubber bands.

## Slide 23: Example
7
3
15
5
2
 | 1 | -1
 | -1 | 1
-7
7
Notes: Let’s recall a little bit math about how it works. Each constraint represent a gaussian distribution. To maximize the likelihood of the joint probability is equal to minimize the summation of the Mahalanobis distance. M-distance means we take the variance into consideration. Now let me give me a glimpse explanation about the role of variance. Take the measurement m02 as example, given its standard deviation, its value added to the matrix will be like this. Smaller sigma, larger weight or larger confident, or larger strength, power in the rubber band.
Let’s set the sigma for m02 as 0.1, which equally increases its weight by ten times. In this case, the constraint m02 will be over-proportional to the other constraints, let’s what will happen.

## Slide 24
7
A: x2 > 5.5
B: x2 = 5.5
C: x2 < 5.5
A: l0 > 12.875
B: l0 = 12.875
C: l0 < 12.875
A: x1 > 8.125
B: x1 = 8.125
C: x1 < 8.125
A: x0 > -2
B: x0 = -2
C: x0 < -2
3
15
5
2
B C C A
= 10
= 0.1
A: x2 > 5.5
B: x2 = 5.5
C: x2 < 5.5
A: l0 > 12.875
B: l0 = 12.875
C: l0 < 12.875
A: x1 > 8.125
B: x1 = 8.125
C: x1 < 8.125
A: x0 > -2
B: x0 = -2
C: x0 < -2
B A A C

## Slide 25: Linear Graph SLAM
Initial Position (absolute constraint)
Motion ( relative odometry constraint)
Measurement (relative landmark constraint)
Trajectory + Map
Notes: Now we have learned the linear graph slam. At start we have initial position, it is a absolute constraint. Then motion, relative odometry constraint, and measurement, relative landmark constraint. We add them into a matrix A and a vector b. But each time the value of the constraint is multiplied by a weight factor, its nothing else but 1/sigma, the uncertainty in motion or measurement. After we done with this adding, we simply compute the mu by inverse A times b. And then its done and outputs the best possible trajectory and along with the map of the landmark.
Now let’s dive into a real robot example.

## Slide 26: https://github.com/rising-turtle/slam_course
Question ?

## Slide 27: Graph SLAM Brief history
Why it becomes popular only recently ?
Linear Graph SLAM
Nonlinear Graph SLAM
  G2O (a general framework for graph optimization )
  ISAM (Incremental Smoothing and Mapping)
Lu, Feng, and Evangelos Milios. "Globally consistent range scan alignment for environment mapping." Autonomous robots4, no. 4 (1997): 333-349.
Notes: Is Graph SLAM a new technique? No, actually, 1997, this is the first time in the robotics literature, the SLAM problem is formulated as a graph model. Since it was proposed about 20 years ago, why it is only become popular recently? A direct answer is efficiency. Direct solve the graph model involves to compute a inverse of a large matrix AtA. In the case of large-scale environment, direct computation of the inverse of the matrix AtA will be very time-consuming.
Recent advancement in sparse linear algebra greatly improves its efficiency. This enables graph slam undergone a renaissance and currently
belong to the state-of-the-art techniques with respect to speed and accuracy. In the next two classes, I will introduce a general framework for graph optimization, g2o, and isam, respectively.
Now let me give you a toy example to understand how the standard graph model works.

## Slide 28: How to solve this problem?
Recall EKF
…
Notes: The robot starts at X0, as it moves to X1 given the odometry measurement U01. Actually x1 has a gaussian distribution, its peak equal to x0 + u01, with some uncertainty. This step is called prediction. Then given the landmark measurement m10, in EKF, it’s called observation, innovation.
We use the red eclipse to represent the value of the uncertainty. This step is called update, which update the robot’s position and uncertainty by using the innovation information. The predict-update loop repeated as the robots moves.
However, in EKF, it only estimate the current pose. The previous poses are marginalized. The advantage is high efficiency, since it has few variables to estimate. The disadvantage is low accuracy, since it can not re-linearize jacobians. As shown in this figure, the initial estimate for a variable x is w0, while its true value is wt. The linear approximation of its jacobian is shown as the slope of this red dash line. This jacobian is quite different from its true model at wt. In this case EKF will produce large error and the filter may diverge quickly.
Recall EKF

## Slide 29: Graph SLAM Problem
Notes: This figure shows a simple example, which gives us a glimpse of the graph structure. The nodes in the graph stand for robot poses and landmark positions. And the edges connecting the nodes are the constraints, either odometry constraint or landmark constraint.
in reality, the process will involve hundreds and thousands of robot poses and landmarks, and also it includes many loops
The structure of the graph will be very complex, then how to solve this problem?

## Slide 30: How to solve the problem?
…
Graph SLAM
Estimate all the robot poses, plus landmarks
Iteratively update robot poses and re-linearize
Notes: In contrast, not only the current robot pose, but also graph slam will estimate all the previous robot poses in a iterative process. This process will iteratively update robot poses, and re-linearize the jacobians given the update variable value. Therefore, it can achieve higher accuracy. As shown in the left figure, the estimation iteratively approaches to wt, where its jacobian is zero, meaning the optimal solution is found.